## Slide 1
Group 5
CT216
Mentor T.A. : Madhav Jivani
Under the Guidance of: Prof. Yash Vasavada
LDPC DECODING FOR 5G NR

## Slide 2
HONOR CODE
We declare that
→ The work that we are presenting is our own work.
→ We have not copied the work (the code, the results, etc.) that someone else has done.
→ Concepts, understanding and insights we will be describing are our own.
→ We make this pledge truthfully. We know that violation of this solemn pledge can carry grave consequences.

## Slide 3
ID | Name | Signature
202301046 | Dhruv Malani | 
202301047 | Jeel Thummer | 
202301049 | Ramoliya Shivam S. | 
202301050 | Siva Suhas Thatavarthy | 
202301051 | Yug Patel | 
ID | Name | Signature
202301052 | Harsh Kakadiya | 
202301053 | Karan Makasana | 
202301054 | Manav Kalavadiya | 
202301055 | Parva Raval | 
202301056 | Darshil Gandhi | 
MEMBERS

## Slide 4
CONTENT
Conclusion
Results
Soft Decision Decoding
Hard Decision Decoding
Encoding
Introduction
1
6
2
4
5
3

## Slide 5
  Low-Density Parity Check (LDPC) codes represent a class of error correcting codes that may be employed for providing error correction of transmission errors in communication systems
  They maintain low decoding complexity due to their sparse matrix structure.
  Using LDPC codes, channel capacities that are close to the theoretical Shannon Limit can be achieved.
INTRODUCTION
LPDC INTRODUCED BY
ROBERT GALLAGER
REDISCOVERY AND ACHIEVEMENT OF SHANNON LIMIT
INDUSTRIAL WORLD ADOPTION
INTEGRATION OF LDPC INTO 5G NR
1962
1990s
2000s
2016-18

## Slide 6
PARITY CHECK MATRIX
BPSK
BASE MATRIX
H MATRIX
FLOW CHART
RANDOM MESSAGE
ENCODED MESSAGE
NOISE
AWGN
RECEIVED MESSAGE
RECEIVED BITS
HARD DECODING
SOFT DECODING

## Slide 7
ENCODING

## Slide 8
BASE GRAPHS
LDPC uses two standard base matrices:
  BG1: Size 46 × 68
  BG2: Size 42 × 52
  These are sparse matrices – mostly 0’s with few non-zero entries
  The base matrices are expanded into the full parity-check matrix (H) using an expansion factor Zc
  The number of message bits is determined by k=m-n where the base graphs are of size m x n. Thus, BG1 has a maximum of 22 bits. BG2 has a maximum of 10 bits.
A general base graph representation

## Slide 9
STRUCTURAL REGIONS OF BASE GRAPHS
Each base matrix is conceptually divided into six logical regions to distinguish between:
  High density / low density
  Information bits / parity bits
Region Breakdown:
Base Graph Region A Region B Region C Region D Region I Region O
BG1 (46×68) 4×22 (A) 4×4 (B) 4×42 (C) 42×22 (D) 42×4 (I) 42×42 (O)
BG2 (42×52) 4×10 (A) 4×4 (B) 4×38 (C) 38×10 (D) 38×4 (I) 38×38 (O)
A: High-density region (important for data mixing)
B: Double diagonal structure – crucial for efficient systematic encoding
C/D: Low-density sections – offer decoding sparsity
I: Identity matrices – help preserve structure in expansion
O: All-zero matrices – act as “gaps” between regions

## Slide 10
A example representation of Base Graph 1 with size 46 X 68

## Slide 11
A example representation of Base Graph 2 with size 42 X 52

## Slide 12
Expansion of Matrix
Each entry from the base matrix expands into a Zc × Zc matrix:
  −1 → Zero matrix
  0 → Identity matrix
k (positive integer) → Zc × Zc identity matrix cyclically right-shifted by k
This process “blows up” the base graph into the full parity-check matrix H
Each base matrix entry the values are from -1,0,1,2,3,4 ..... Zc-1
Values mentioned in the figure are the expansion values that can be taken by the base graphs

## Slide 13
PARITY CHECK MATRIX (H)
LDPC codes are defined by a sparse matrix H, constructed from base matrices using expansion factor Zc
A example for expansion from Base Matrix with expansion factor : 4

## Slide 14
CODE RATE AND RATE MATCHING
Defined as the ratio of message bits to total transmitted bits
Rc = K/N
K: Message bits
N: Total transmitted bits
Rate Matching:
It is the process of adjusting the number of bits transmitted to match the desired code rate and channel capacity.
  It allows flexible adaptation to varied data rates, block sizes, and channel conditions.
  Even if the LDPC encoder always generates the same number of output bits , rate matching helps us transmit only as many as needed.
There are some rate matching techniques
    Puncturing
    Shortening

## Slide 15
MESSAGE BIT SHORTENING
  Set some message bits to zero and do not transmit them.
  The S shortened bits are not transmitted, effectively increasing K and N, which results in a decreased Rc
  Decoder treats shortened bits as known-zero bits.
  Implemented by removing those columns from the H matrix
Decoding Behavior:
  Corresponding columns in H are disregarded

## Slide 16
MESSAGE BIT PUNCTURING
  Skip transmitting certain encoded bits of the H matrix
  At the receiver, missing bits are filled with zeros or soft-value 0 during decoding.
  The first 2Z message bits are never transmitted
  These bits are highly connected → prone to cause decoding errors
  Helps avoid error propagation without changing Rc
  These bits are included in H during decoding

## Slide 17
PARITY BIT PUNCTURING
  Certain parity bits are not transmitted from the H matrix
  Reduces total bits N, resulting in a higher code rate
  Corresponding columns in H are disregarded during the decoding
  Alternatively, set r = 0 for punctured parity bits

## Slide 18
  Suppose you have a base matrix of size m x n and an expansion factor of z. So the possible length of the codeword will be n*z.
  Out of these n*z bits, the first 2z are always punctured. So we have (n-2)*z bits left.
  Suppose you want to achieve an overall code rate of x/y
    Assume that you puncture a*z bits out of the available (n-2)*z bits.
    Number of message bits = (n-m) * z.
    From the equation shown, we can compute the number of parity bits required
  So, the required size of H matrix is
    Number of rows = Number of parity bits which we get from the equation
    Number of columns = Number of columns from equation + 2
CODE RATE MATCHING FORMULA
derived formula of code rate matching

## Slide 19
RATE MATCHING EXAMPLE
  Example: We want Code Rate = 3/4 with Base Matrix 46 × 68
  Suppose we have a 46 X 68 Base matrix and we want a code rate of 3/4.
  So, n = 68, m= 46, x = 3, y = 4.
  Putting these values in the previous equation and solving for a, we get a = 49
  So, now we have to transmit 66z - 49z = 17z bits in all.
  Out of these 17z bits, 13z are message bits.
  Parity bits sent: 17z−13z=4z
  Rows used: Number of parity bits = 4
  Columns used: Transmitted bits = 17+2=19
for a code rate of ¾ we use a 4 x19 submatrix from the full 46 X 68 base matrix

## Slide 20
  We exploit the structure of the base matrix to do the encoding
  The main idea behind the decoding is that all the parity bits greater than equal to 5 can be obtained simply by solving a linear equation because of the structure of the matrix
  To find the first four bits, we need to solve 4 equations simultaneously. This calculation is made easy due to the double-diagonal structure of the matrix.
  We will consider an example to understand the encoding:
    We have a message vector m = [m1 m2 m3 m4 m5]
    4 parity bits are added to this vector which are [p1 p2 p3 p4]
    Codeword = [c1 c2 c3 c4 c5 c6 c7 c8 c9]
ENCODING USING BASE MATRIX
double diagonal stucture

## Slide 21
Equations obtained:
  I₁v₁ + I₃v₃ + I₁v₄ + I₂v₅ + Iv₆ = 0 -Equation 1
  I₂v₁ + Iv₂ + I₃v₄ + Iv₆ + Iv₇ = 0 -Equation2
  I₄v₂ + I₂v₃ + Iv₄ + I₁v₅ + Iv₇ +Iv₈ = 0 -Equation 3
  I₄v₁ + I₁v₂ + Iv₃ + I₂v₅ +Iv₈ = 0 -Equation 4
  Adding all four equations:
    I₁v₅ = I₁v₁ + I₂v₁ + I₄v₁ + Iv₂ + I₄v₂ + I₁v₂ + I₃v₃ + I₂v₃ + Iv₃ + I₁v₄ + I₃v₄ + Iv₄
  We know that [v₁ v₂ v₃ v₄ v₅ v₆ v₇ v₈ v₉] = [m₁ m₂ m₃ m₄ m₅ p₁ p₂ p₃ p₄]
  So, rewriting the equation, we get:
    I₁p₁ = I₁m₁ + I₂m₁ + I₄m1 + Im₂ + I₄m₂ + I₁m₂ + I₃m₃ + I₂m₃ + Im₃ + I₁m₄ + I₃m₄ + Im₄
  From here we can get p₁.
  Substitute it in equation1 to get p₂ and solve so on to get all the 4 parity bits
  The encoded message must satisfy the equality H*c = 0.
  After calculating the first 4 parity bits it is easy to calculate the other parity bits as for the each column only one parity bit is present others get 0 (after multiplied)
After getting the parity bits we need to do BPSK and add noise using the AWGN channal

## Slide 22
BPSK MODULATION
Binary Phase Shift Keying (BPSK) maps bits to voltages:
  Bit 0 → +1 volt
  Bit 1 → −1 volt
Mapping formula:
s = 1 − 2b, where b is the bit and s is the modulated signal
  Ensures maximum symbol separation for better noise resistance

## Slide 23
Simulates real-world noise using Additive White Gaussian Noise (AWGN)
  Noise power determined by SNR:
  γ = Eₛ / N₀, where Eₛ is signal energy
  σ² = 1 / γ, noise variance
Received signal:
  r = s + u, where u = σ × uₛ
  uₛ ~ N(0, σ) (standard normal noise)
  AWGN affects BPSK symbols, testing decoder robustness
AWGN CHANNEL
schematic of bpsk and awgn channal

## Slide 24
DECODING

## Slide 25
DECODING TANNER GRAPH
  The Parity Check Matrix H can be represented by a Bipartite Graph containing 2 types of nodes :- (i) Variable nodes or Bit nodes (VN’s) , (ii) Check nodes(CN’s) to check parity , this is called as Tanner graph .
  A Sample Parity Check Matrix H
  Corresponding Tanner Graph of given H

## Slide 26
Hard Decision Decoding
DECODING ALGORITHMS
Soft Decision Decoding
Operates on bits(0/1)
  Bit Flipping Algorithm
  Weighted BF Algorithm
  and More Complexities in BF Algorithm
Operates on LLRs (Real Valued Beliefs)
  Belief Propagation Algorithm
  Min-Sum Algorithm
  Layered Decoding
  Neural Decoding

## Slide 27
HARD DECISION DECODING
Hard Decision Performance:-
ĉᵢ = 0 if rᵢ > 0
1 else
  rᵢ is the received value from the channel
  Convert all the soft values to binary by thresholding at 0:
  If rᵢ is positive (closer to +1), assume bit was 0
  If rᵢ is negative (closer to −1), assume bit was 1
Steps:-
  Compute the syndrome vector, s = H * ĉ^T mod 2
  For each bit:
Check if it's part of many unsatisfied parity checks, and flip it if found.
  Repeat until:
Syndrome = 0 (all parity checks satisfied) or Maximum iterations reached
Bit Flipping Algorithm

## Slide 28
HARD DECISION DECODING
Bit Flipping Algorithm
  Message from VNi to CNj
Each variable node VNi​ transmits its current hard-decision value to all connected check nodes CNj based on the parity-check matrix H.
  Message from CNj to VNi
Each check node CNj evaluates the local parity constraint and sends a binary indication to each connected variable node VNi​, indicating it might be incorrect.
  Bit-Flipping Criterion at VNi​
If more than 50% of the connected check nodes CNj indicate a parity violation, the bit value of VNi​ is inverted, this process iterates until convergence or until maximum iteration limit is reached.

## Slide 29
SOFT DECISION DECODING
Step 1: VN to CN Message(Current belief)
Min Sum Approximation
Input:
  Real values from channel are represented as soft bits (LLRs):
Step 2: CN to VN Message (Min-Sum)
Step 3: Update Total LLR for Each Bit
Bit Decision Rule:
ĉᵢ = 1, if L(Qi) < 0
0, else
Stopping Condition:
  Max iterations done OR
  H⋅ĈT = 0 (all parity checks satisfied)

## Slide 30
SOFT DECISION DECODING
Storage matrix ℓ is a sparse matrix of same size as Parity Check Matrix.
ℓ(i,j)=0 if H(i,j)=0 and
ℓ(i,j) is non-zero only if H(i,j)=1
For Each Row:
Magnitude
  min1 = minimum absolute value of all non-zero entries in row
  min2 = next higher absolute value
  Set magnitude of all values except minimum = min1
  Set magnitude of minimum value = min2
Sign
  Parity = Product of signs of entries in row
  New sign of entry = (old sign) (parity)
Min Sum Approximation Algorithm

## Slide 31
SOFT DECISION DECODING
Example

## Slide 32
SOFT DECISION DECODING
Example

## Slide 33
SOFT DECISION DECODING
For Each Column
New Values
  Sumj = rj + sum of all entries in column j.
  New Entry = Sum - (Old Entry)
  Sum is the new belief generated about values after the ith iteration
Decoding Values
  If sumj > 0, decision on bit j = 0
  If sumj < 0, decision on bit j = 1
Min Sum Approximation Algorithm

## Slide 34
SOFT DECISION DECODING
Example
After Column Operation
Updated
Belief

## Slide 35
RESULT OF
NR_2_6_52

## Slide 36
CODE RATE = 1/4
HARD DECODING
SOFT DECODING

## Slide 37
HARD DECODING
SOFT DECODING

## Slide 39
CODE RATE = 1/3
HARD DECODING
SOFT DECODING

## Slide 40
HARD DECODING
SOFT DECODING

## Slide 42
CODE RATE = 1/2
HARD DECODING
SOFT DECODING

## Slide 43
HARD DECODING
SOFT DECODING

## Slide 45
CODE RATE = 3/5
HARD DECODING
SOFT DECODING

## Slide 46
HARD DECODING
SOFT DECODING

## Slide 48
RESULT OF
NR_1_5_352

## Slide 49
CODE RATE = 1/3
HARD DECODING
SOFT DECODING

## Slide 50
HARD DECODING
SOFT DECODING

## Slide 52
CODE RATE = 1/2
HARD DECODING
SOFT DECODING

## Slide 53
HARD DECODING
SOFT DECODING

## Slide 55
CODE RATE = 3/5
HARD DECODING
SOFT DECODING

## Slide 56
HARD DECODING
SOFT DECODING

## Slide 58
CODE RATE = 4/5
HARD DECODING
SOFT DECODING

## Slide 59
HARD DECODING
SOFT DECODING

## Slide 61
SHANNON’S LIMIT

## Slide 62
THANK YOU